## Slide 1: Lightweight Hardware Transactional Memory Profiling
Qingsen Wang, Pengfei Su, Xu Liu
College of William & Mary
Milind Chabbi
Scalable Machines Research

## Slide 2: Synchronization in Parallelism
  Pessimistic Concurrency Control
    Lock
  Optimistic Concurrency Control
    Transactional Memory (TM)
T1
TM_begin()
TM_end()
TM_end()
T2
TM_begin()
TM_begin()
T3
TM_end()
abort
retry
lock()
unlock()
T1
T2
lock()
wait()
unlock()
Software Transactional Memory (STM)
Hardware Transactional Memory (HTM)

## Slide 3: Hardware Transactional Memory
  Working principle
  Abort reason
    Conflict abort
    Capacity abort
    Synchronous abort
Save a snapshot of current state
Store any change in cache (invisible to others)
Any concurrency requirement violated?
Restore the snapshot
Make changes visible to others
Y
N
Commit
Abort
Threads contend for the same cache line
Accessed memory > hardware supported max size
System calls, special instructions, etc.

## Slide 4: Hardware Transactional Memory
  Workflow
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code
LOCK();
// user code
UNLOCK();
HTM path
Fallback path
Critical section
TM_BEGIN;
// user code
TM_END;

## Slide 5: Hardware Transactional Memory
  HTM needs support from profiling tools
  Tools for Software Transaction Memory (STM)?
    Hard to directly monitor hardware behavior
    New types of aborts (e.g., capacity abort, synchronous abort)
  We need a profiler designated for HTM
    Does a program spend a lot of time in transactions?
    Is a transaction benign?
    Which part of a transaction contributes to the most of execution time?
    Why and where causes the abort?
    How to improve the performance of a transaction?

## Slide 6: Existing Work
  TSXProf
    Record HTM execution timestamps from instrumentation
    Replay in software for contention analysis
  Perf, VTune
    PMU sampling
    Record HTM status from hardware hint (e.g., conflict abort? capacity abort?)
Large overhead
Emulation Reality
Not enough information for analysis

## Slide 7: Solution – TxSampler
  Lightweight
    ~4%(time)
    <5MB/thread (memory)
  Insightful
Time decomposition
Abort analysis
Contention Identifying

## Slide 8: TxSampler – How it works
Sample from hardware events
Resolve callstack
Attribute metric

## Slide 9: TxSampler – How it works
  Performance Monitor Units
    PMU
    Monitor hardware events
      CPU cycles, TX commit/abort, memory load/store
    Interrupt every N occurrences of a monitored event
      N is a preset sampling period
      One interrupt one sample
Sample from hardware events
Resolve callstack
Attribute metric

## Slide 10: Solution – TxSampler
Sample from hardware events
Resolve callstack
Attribute metric
  Callstack unwinding

## Slide 11: Solution – TxSampler
  Increment corresponding metrics under current callstack
    Statistical attribution, NOT for individual transactions
Sample from hardware events
Resolve callstack
Attribute metric

## Slide 12: Novice Guide
CS is long?
High TX overhead
Analyze time decomposition
large
large
large
large
no
yes
Analyze abort type
Redesign algorithm
Split transactions
Shrink transactions
Relocate data to share cache lines
Conflicts caused by shared data
Footprint large
high conflict aborts
high capacity aborts
high sync aborts
Shared data contention
False sharing
Unfriendly instructions/call inside transaction
Relocate data to different cache lines
Relocate data based on threads.
Redesign algorithm
Shrink transactions
Split transactions
Move unfriendly instructions/call out from transaction
Use a friendly equivalent
Merge small transactions
yes
no
START
Find a place (function, transaction, loop, line, etc.) with largest abort/commit, abort number, abort weight, , , etc.
High lock waiting
Elide read lock
Use fine-grained locks to serialize
No HTM-related issues
Time Analysis
Abort Analysis
Metrics to investigate
Symptoms
Optimization suggestion

## Slide 13: Challenge I – Callstack inside HTM
  How sampling works
main program
profiler routine
PMU Sample
Retrieve callstack here
Attribute metrics
suspend
resume

## Slide 14: Challenge I – Callstack inside HTM
  How sampling works
main program
TM_BEGIN
PMU Sample A
HTM path
fallback path
TM_END
PMU Sample B
Retrieve callstack here
Attribute metrics
suspend
resume
profiler routine
Trustworthy?

## Slide 15: Challenge I – Callstack inside HTM
  Last Branch Records (LBRs)
    Record most recently executed branches
    Each entry contains
      “from” address
      “to” address
      flags of execution states

## Slide 16: Challenge I – Callstack inside HTM
  Reconstruct callstack
void A(){
TM_BEGIN;
B();
C();
TM_END;
}
int main(void){
A();
return 0;
}
void D(){
...
//POINT X
...
}
void C(){
D();
}
void B() {
D();
}
PMU sample
Call stack unwinding
main()A()B()
Index | Content | Content | abort | abort | in-htm | in-tsx
0 | Call IR handler | Call IR handler | 1 | 1 | 0 | 0
1 | Call D | Call D | 0 | 0 | 1 | 1
2 | Call C | Call C | 0 | 0 | 1 | 1
3 | B return | B return | 0 | 0 | 1 | 1
4 | D return | D return | 0 | 0 | 1 | 1
5 | Call D | Call D | 0 | 0 | 1 | 1
6 | Call B | Call B | 0 | 0 | 1 | 1
... (related to TM setting) … |  |  |  |  |  | 
… | Call A |  |  | 0 |  | 0
Retrieve LBRs
main()A()C()->D()
C()->D()

## Slide 17: Challenge II – Time Decomposition
Critical Section
Chart: 
| InHTM | inFallback | inLockWaiting | inOverhead
销售额 | 25 | 25 | 25 | 25
inHTM
inFallback
inLockWaiting
inOverhead

## Slide 18: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 19: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 20: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 21: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 22: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 23: Challenge II – Time Decomposition
  inCS = inHTM + inFallback + inLockWaiting + inOverhead
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code

## Slide 24: Challenge II – Time Decomposition
  HTM library adds thread-local status flags
Wait for lock to be free
Start
Succeed?
Retry?
Finish
Begin HTM
Acquire the lock
Release the lock
N
N
Y
Y
User code
End HTM
User code
inLockWaiting = true
inLockWaiting = false

## Slide 25: Challenge II – Time Decomposition
  Profiler routine queries the status flags to attribute the corresponding metric
if (inLockWaiting) {
cur_context.timeInLockWaiting++;
}

## Slide 26: HTMBench
PARSEC3/netstreamcluster, QuakeTM, PBZip2, BART/nufft, stamp/ssca, RMS-TM/ScalParc, splash2/raytrace splash2/barnes, splash2/fmm, splash2/ocean, splash2/water | BerkeleyDB, Memcached, Parboil/histo, RMS-TM/UtilityMine, SSCA2, NPB/ua, PARSEC2/dedup, PARSEC3/netdedup, PARSEC3/netferret | 
 | LevelDB, AVLTree, syncrho/linkedlist, synchro/skiplist, bplustree, Lee-TM, KyotoCabinet, stamp/yada, stamp/intruder, stamp/vacation, stamp/kmeans, stamp/genome, stamp/labyrinth | 
PARSEC3/netstreamcluster, QuakeTM, PBZip2, BART/nufft, stamp/ssca, RMS-TM/ScalParc, splash2/raytrace splash2/barnes, splash2/fmm, splash2/ocean, splash2/water | BerkeleyDB, Memcached, Parboil/histo, RMS-TM/UtilityMine, SSCA2, NPB/ua, PARSEC2/dedup, PARSEC3/netdedup, PARSEC3/netferret | 
 | LevelDB, AVLTree, syncrho/linkedlist, synchro/skiplist, bplustree, Lee-TM, KyotoCabinet, stamp/yada, stamp/intruder, stamp/vacation, stamp/kmeans, stamp/genome, stamp/labyrinth | 
>30 benchmarks

## Slide 27: Optimization
Program | Symptoms | Solutions | Speedup
dedup* | high capacity abort | refine hash table | 1.20X
 | high synchronous aborts | remove system calls | 
avl tree | high | elide read lock | 1.21X
histo* | high | merge transactions | 2.95X
 | severe false sharing | sort the input array | 
ua | high | merge transactions | 1.05X
vacation | high abort rate | reduce transaction size | 1.21X
leveldb* | high abort rate | split transactions | 1.05X
ssca2* | high | merge transactions | 1.10X
netdedup* | high conflict abort | shrink transactions | 2.60X
 | high synchronous aborts | remove system calls | 
linkedlist* | high abort rate low average abort penalty | limit transaction size with auxiliary locks 3.78X | 3.78X
Program | Symptoms | Solutions | Speedup
dedup* | high capacity abort | refine hash table | 1.20X
 | high synchronous aborts | remove system calls | 
avl tree |  | elide read lock | 1.21X
histo* |  | merge transactions | 2.95X
 | severe false sharing | sort the input array | 
ua |  | merge transactions | 1.05X
vacation | high abort rate | reduce transaction size | 1.21X
leveldb* | high abort rate | split transactions | 1.05X
ssca2* |  | merge transactions | 1.10X
netdedup* | high conflict abort | shrink transactions | 2.60X
 | high synchronous aborts | remove system calls | 
linkedlist* | high abort rate low average abort penalty | limit transaction size with auxiliary locks 3.78X | 3.78X
* newly found

## Slide 28: Case Study – Dedup
  Compresses data via deduplication
  Consists of three major stages
    ChunkProcess
    FindAllAnchors
    Compress
  Runs with 4 threads per major stage

## Slide 29: Case Study – Dedup
  Time analysis
Chart: 
| Non-critical section | TX | Fallback | Lockwaiting | Overhead
Time Decomposition | 62 | 4.95 | 3.19 | 29.66 | 0.2

## Slide 30: Case Study – Dedup
  Abort analysis
    High capacity aborts
    High synchronous aborts

## Slide 31: Case Study – Dedup
  Abort analysis
    High capacity aborts
    High synchronous aborts
Abort weight
Capacity abort
Pseudo node
In HTM

## Slide 32: Case Study – Dedup
  Abort analysis
    High capacity aborts
    High synchronous aborts
X
Bin utilization: 2.2%
X
Bin utilization: 82%

## Slide 33: Case Study – Dedup
  Abort analysis
    High capacity aborts
    High synchronous aborts

## Slide 34: Case Study – Dedup
  Abort analysis
    High capacity aborts
    High synchronous aborts

## Slide 35: Case Study – Dedup
  Optimization benefit
    Capacity aborts: 97% ↘
    Synchronous aborts: 26% ↘
    Speedup: 1.20X

## Slide 36: Case Study – Dedup

## Slide 37: Conclusion
  TxSampler
    A sampling-based lightweight call path profiler for HTM programs
    Provides insights of time decomposition, aborts, commits and memory contention
    Open sourced, https://github.com/ScalableMachinesResearch/TxSampler
  HTMBench
    Over 30 benchmarks
    Open sourced, https://github.com/ScalableMachinesResearch/HTMBench
  Optimization
    Dedup
Questions?